## Slide 1: FINN Deep Dive: HW Scheduling & Folding
Giulio Gambardella, Yaman Umuroglu
Last updated 2020-06-05

## Slide 2: Previously on FINN
Hardware architecture is dataflow with streaming
  HLS streams (FIFOs) are used to communicate among layers
  Each layer is always running, starts computing as soon as it can
  Each layer has internal parallelism s.t. pipeline is approximately balanced

## Slide 3: Data Layout & Scheduling Preliminaries
Carefully select folded (time-multiplexed) data layout
  Match producer and consumer order to minimize buffering + latency
Carry everything between layers using hls::stream< >
  Stream width depends on precision and degree of parallelization
  Use data width converters to up/downscale where needed
Specify parallelism (P) instead of folding (or reuse) factor (F)
  Amount of work (W) = parallelism (P) * folding factor (F)

## Slide 4: FINN Tensor Layout: NHWFP
Variant of NHWC = ( N (batch), H (height), W (width), C (channels) )
  Channels from same pixel ‘next to’ each other, simplifies e.g. sliding window
  C is dot product axis, may contain more than just channels (e.g. lowered convolution)
  Almost all hlslib layer implementations assume this layout, but there are exceptions
N is 1 from the perspective of our hardware
  H and W can be omitted for FC layers (equal to 1)
Add time-multiplexing axis on top of NHWC
  Let C = F * P where F (folding) and P (parallelism) are integers
  Layout becomes (N, H, W, F, P)
This decides the stream width: P elements every cycle
  Elements may be e.g 2-bit, will be packed tightly together

## Slide 5: The Basics: Matrix-Vector Folding for a FC Layer
Assume these dimension sizes:
  W = number of input features
  H = number of output features
Two controllable degrees of parallelism:
  MACs inside a single inner product: SIMD
  Inner products in parallel: PE
  H % PE == 0, W % SIMD == 0
W (input features)
H (output features)

## Slide 6: The Basics: Matrix-Vector Folding in Hardware
PE and SIMD will control…
  Performance
  ‘Native’ input/output stream widths
  Hardware resources (unrolled for loops):
    Post-synth LUT
‘native’ input stream width:
SIMD * input precision
Original tensor shape:
(1, W)
Folded tensor shape:
(1, W/SIMD, SIMD)
‘native’ output stream width:
PE * output precision
Original tensor shape:
(1, H)
Folded tensor shape:
(1, H/PE, PE)

## Slide 7: The Basics: Matrix-Vector Folding, Cycle 1
X
=
PE
SIMD
SIMD
PE
(partial result in accumulators)
Assume PE = H / 2, SIMD = W / 2
Read from input stream
Save in OCM buffer

## Slide 8: The Basics: Matrix-Vector Folding, Cycle 2
X
=
PE
SIMD
SIMD
PE
Read from input stream
Save in OCM buffer
Write result to output stream

## Slide 9: The Basics: Matrix-Vector Folding, Cycle 3
X
=
PE
SIMD
SIMD
(reused from OCM buffer)
PE
(partial result in accumulators)

## Slide 10: The Basics: Matrix-Vector Folding, Cycle 4
X
=
PE
SIMD
SIMD
(reused from OCM buffer)
PE
Finished!
Took 4 cycles
Write result to output stream

## Slide 11: FINN I/O – main ideas
All layers consumes input in the same order
  All channels for 1 pixel, pixels in raster order
All layers generates output in the same order used to consume from next layer
  In order to decrease buffering requirements among layers (FIFOs)
  No need of data restructuring among layers (im2col performed inside the layer with line buffering)

## Slide 12: FINN – I/O order
Conv Layer 0
IFM
Weight buffer
Conv Layer 1
Weight buffer
OFM
Height
Width
Channels

## Slide 13: FINN – I/O order
Conv Layer 0
IFM
Weight buffer
Conv Layer 1
Weight buffer
OFM
Height
Width
Channels

## Slide 14: FINN – I/O order
Conv Layer 0
IFM
Weight buffer
Conv Layer 1
Weight buffer
OFM
Height
Width
Channels

## Slide 15: FINN – I/O order
Conv Layer 0
IFM
Weight buffer
Conv Layer 1
Weight buffer
OFM
Height
Width
Channels

## Slide 16: Folding compute on fixed PE array

## Slide 17: Convolutional layer – folding
Height
Width
Channels
.
.
.
PE output pixels are generated every cycles
cycles to complete
SIMD
PE
PE
SIMD

## Slide 18: Im2col + matrix vector = convolution
Lowering convolution to im2col + matrix multiplication
Performed in a streaming function without buffering of the whole feature map
  Produces input for matrix operation as soon as data is available

## Slide 19: Animation of folding in a Conv2D

## Slide 20: Matrix Vector streaming execution in a Matrix Matrix (rpt)
OFM0
OFM1
OFM2
OFM3
Execution matrix-matrix:
For (OFDim*OFMDim)
  Execute Matrix-Vector
IFM0
IFM2
IFM1
IFM3

## Slide 21: Neuron1 Synapse1
IFM0
IFM2
IFM1
IFM3
Execution matrix-vector:
First neuron
  For (SynapseFolding)
    Read SIMD Input pixels
    Compute matrix Vector in each PE
OFM0
OFM1
OFM2
OFM3

## Slide 22: Neuron1 Synapse2
IFM0
IFM2
IFM1
IFM3
Execution matrix-vector:
First neuron
  For (SynapseFolding)
    Read SIMD Input pixels
    Compute matrix Vector in each PE
OFM0
OFM1
OFM2
OFM3

## Slide 23: Neuron1 Synapse3
IFM0
IFM2
IFM1
IFM3
OFM0
OFM1
OFM2
OFM3
Execution matrix-vector:
First neuron
  For (SynapseFolding)
    Read SIMD Input pixels
    Compute matrix Vector in each PE

## Slide 24: Neuron1 Synapse4
IFM0
IFM2
IFM1
IFM3
OFM0
OFM1
OFM2
OFM3
Execution matrix-vector:
First neuron
  For (SynapseFolding)
    Read SIMD Input pixels
    Compute matrix Vector in each PE

## Slide 25: Neuron1 Synapse5
IFM0
IFM2
IFM1
IFM3
OFM0
OFM1
OFM2
OFM3
Execution matrix-vector:
First neuron
  For (SynapseFolding)
    Read SIMD Input pixels
    Compute matrix Vector in each PE

## Slide 26: Neuron1 Synapse6
IFM0
IFM2
IFM1
IFM3
OFM0
OFM1
OFM2
OFM3
Execution matrix-vector:
First neuron
  For (SynapseFolding)
    Read SIMD Input pixels
    Compute matrix Vector in each PE

## Slide 27: Neuron1 Synapse7
IFM0
IFM2
IFM1
IFM3
OFM0
OFM1
OFM2
OFM3
Execution matrix-vector:
First neuron
  For (SynapseFolding)
    Read SIMD Input pixels
    Compute matrix Vector in each PE

## Slide 28: Neuron1 Synapse8
IFM0
IFM2
IFM1
IFM3
OFM0
OFM1
OFM2
OFM3
Execution matrix-vector:
First neuron
  For (SynapseFolding)
    Read SIMD Input pixels
    Compute matrix Vector in each PE

## Slide 29: PE Pixels output
IFM0
IFM2
IFM1
IFM3
Execution matrix-vector:
First neuron
  For (SynapseFolding)
    Read SIMD Input pixels
    Compute matrix Vector in each PE
  Threshold comparison
  Output PE Pixels
OFM0
OFM1
OFM2
OFM3

## Slide 30: Neuron2 Synapse1
IFM0
IFM2
IFM1
IFM3
Execution matrix-vector:
First neuron
  For (SynapseFolding)
    Read SIMD Input pixels
    Compute matrix Vector in each PE
  Threshold comparison
  Output PE Pixels
Other neurons
  For (SynapseFolding)
    Read buffered SIMD pixels
    Compute matrix Vector in each PE
OFM0
OFM1
OFM2
OFM3

## Slide 31: Neuron2 Synapse2
IFM0
IFM2
IFM1
IFM3
OFM0
OFM1
OFM2
OFM3
Execution matrix-vector:
First neuron
  For (SynapseFolding)
    Read SIMD Input pixels
    Compute matrix Vector in each PE
  Threshold comparison
  Output PE Pixels
Other neurons
  For (SynapseFolding)
    Read buffered SIMD pixels
    Compute matrix Vector in each PE

## Slide 32: Neuron2 Synapse3
IFM0
IFM2
IFM1
IFM3
OFM0
OFM1
OFM2
OFM3
Execution matrix-vector:
First neuron
  For (SynapseFolding)
    Read SIMD Input pixels
    Compute matrix Vector in each PE
  Threshold comparison
  Output PE Pixels
Other neurons
  For (SynapseFolding)
    Read buffered SIMD pixels
    Compute matrix Vector in each PE

## Slide 33: Neuron2 Synapse4
IFM0
IFM2
IFM1
IFM3
OFM0
OFM1
OFM2
OFM3
Execution matrix-vector:
First neuron
  For (SynapseFolding)
    Read SIMD Input pixels
    Compute matrix Vector in each PE
  Threshold comparison
  Output PE Pixels
Other neurons
  For (SynapseFolding)
    Read buffered SIMD pixels
    Compute matrix Vector in each PE

## Slide 34: Neuron2 Synapse5
IFM0
IFM2
IFM1
IFM3
OFM0
OFM1
OFM2
OFM3
Execution matrix-vector:
First neuron
  For (SynapseFolding)
    Read SIMD Input pixels
    Compute matrix Vector in each PE
  Threshold comparison
  Output PE Pixels
Other neurons
  For (SynapseFolding)
    Read buffered SIMD pixels
    Compute matrix Vector in each PE

## Slide 35: Neuron2 Synapse6
IFM0
IFM2
IFM1
IFM3
OFM0
OFM1
OFM2
OFM3
Execution matrix-vector:
First neuron
  For (SynapseFolding)
    Read SIMD Input pixels
    Compute matrix Vector in each PE
  Threshold comparison
  Output PE Pixels
Other neurons
  For (SynapseFolding)
    Read buffered SIMD pixels
    Compute matrix Vector in each PE

## Slide 36: Neuron2 Synapse7
IFM0
IFM2
IFM1
IFM3
OFM0
OFM1
OFM2
OFM3
Execution matrix-vector:
First neuron
  For (SynapseFolding)
    Read SIMD Input pixels
    Compute matrix Vector in each PE
  Threshold comparison
  Output PE Pixels
Other neurons
  For (SynapseFolding)
    Read buffered SIMD pixels
    Compute matrix Vector in each PE

## Slide 37: Neuron2 Synapse8
IFM0
IFM2
IFM1
IFM3
Execution matrix-vector:
First neuron
  For (SynapseFolding)
    Read SIMD Input pixels
    Compute matrix Vector in each PE
  Threshold comparison
  Output PE Pixels
Other neurons
  For (SynapseFolding)
    Read buffered SIMD pixels
    Compute matrix Vector in each PE
OFM0
OFM1
OFM2
OFM3

## Slide 38: PE Pixels output
IFM0
IFM2
IFM1
IFM3
Execution matrix-vector:
First neuron
  For (SynapseFolding)
    Read SIMD Input pixels
    Compute matrix Vector in each PE
  Threshold comparison
  Output PE Pixels
Other neurons
  For (SynapseFolding)
    Read buffered SIMD pixels
    Compute matrix Vector in each PE
  Threshold comparison
  Output PE Pixels
OFM0
OFM1
OFM2
OFM3